## Slide 1: Lab 4: Memory Mapped I/O
CS341

## Slide 2: How does Arduino communicate with I/O ports?
Memory Mapped I/O vs Port Mapped I/O
  Memory Mapped: I/O space in on same chip as RAM
  Port Mapped: I/O space in separate chip
  Similar Comparison between Harvard vs Von Neumann
  Port mapped is faster as data and address bus do not have to be shared.
    However because it is not shared, handling I/O is more tedious
    Similar to us looking at EEPROM while talking to RAM
  Memory Mapped allows us to manipulate I/O easier.
    Simpler to design than port mapped
    However, takes up room we could use for more data.
  Arduino uses memory mapped. Keeps small amount of space in RAM for each pin
Pins

## Slide 3: Today’s Lab: Lab 1 without Arduino provided digitalWrite()
Look closer into how memory mapped I/O works
Determine which bits in RAM/Memory control pin 13
  Use provided displayRAM function
  Toggle a bit
Blink an LED, again.
To review, take array4 in RAM HEAP from lab3:
350: . 3 `. . . . . .A r r a y 4 .
350: 33 30 60 03 00 00 08 00 41 72 72 61 79 20 34 00
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0
Bit 7
Bit 6
Bit 5
Bit 4
Bit 3
Bit 2
Bit 1
Bit 0
Address: 358 359 35A 35B 35C 35D 35E

## Slide 4: Organization of Pins
Multiple pins are stored in the same port
  A port is where we receive input or send output
  Controls where to send or not to send current
Port D has 3 corresponding registers that control pins 0-7
The bits that correspond to a given pin are organized by purpose, not by pin
Each pin has 3 bits used to control it.
  Data register
    Where we write to
    0 no current 1 current running to pin
  Data Direction Register
    Control direction of data
    0 input, 1 output
  Input Pins
    Where we read from
    0 no input 1 input received
Digital Pin 3’s Bits

## Slide 5: Memory mapped I/O space above the registers before Ram
We don’t address the port registers themselves, instead we use spots reserved for accessing these port registers in ram
The RAM memory addresses used for digital pins 2 through 13 are located between locations 0x20 and 0x2f. Only the cpu can manipulate the actual I/O registers directly.
The first step of today’s lab is finding the memory address that corresponds to the port that holds pin 13 bits

## Slide 6: Interfacing with a digital pin
USING PROVIDED FUNCTIONS
pinMode(int pin, OUTPUT);
pinMode(int pin, INPUT);
digitalWrite(int pin, HIGH);
digitalWrite(int pin, LOW);
digitalRead(int pin);
DIRECTLY USING MEMORY ADDRESSES
Set data direction bit to 1
Set data direction bit to 0
Set data bit to 1
Set data bit to 0
Check value of input bit
-By using displayRam, we can use this to locate the specific bits of pin

## Slide 7: Blinking LED manually
Let’s say that the address for writing to pin 7 is 0x50 and the correct bit is the 6th bit
  0100 00002
Then, this code sets pin 7 to HIGH
And this code turns pin 7 on and off for 1 second each
*Note last line is equivalent *pin7 = 0x80
A number xor’d with itself is always 0
0 xor’d with a number is always that number:
1000000^1000000 = 0000000
1000000^0000000= 1000000