## Slide 1: Lab 6: Analog and Digital input
CS444 2021

## Slide 2: Today’s Lab:
Through arduino, you will create a light that turns on with motion. You will use:
  A motion sensor (to detect motion
  A light sensor (to determine if the light is already on)
To code:
  Read digital input from motion sensor
    If motion, read from analog input from sensor
    If no light, turn light on
  If no motion, turn light off

## Slide 3: Example:

## Slide 4: Component of Today: Infrared Motion Sensor
Send digital output:
  1 = movement
  0 = no movement
Detects motion by looking at changes in heat
  Looks for changes in temperature.
  Body heat is infrared energy

## Slide 5: Component of Today: Photoresistor
A variable resistor that changes based on light detection
Gives off analog output:
  A voltage between 0V and 5V
Analog Pins
Reads a value between 0V and 5V
In this code, Adruino interprets it as a value between 0 - 1023
Can also be used as digital pins
To read an output from an analog component:
  analogRead(AO)

## Slide 6: What you’ll do:
Complete the circuit
Implement the logic in loop()
  Loop() {
  if (motion) {
  if (light < 200) {
  // light bulb on
  }
  } else {
  //turn the light off if there's no motion
  }
  delay(200);
  }